HatchSafe® Specifications

- GENERAL

  - SECTION INCLUDES

    - Specialty custom designed HatchSafe® for roof hatch openings, including,

      - HatchSafe® - Model Numbers:  HSF-4848M, HSF-4866M, HSF-4884M, HSF-5448M, HSF-5466M, HSF-5484M,

      - Patent Numbers:  6,095,283; 6,347,685; 6,619,428) horizontal grab bars to ensure a firm, stable grip when exiting/entering the roof hatch.

  - RELATED SECTIONS

    - Section 077233 – Roof Hatches

    - Section 055213 – Pipe and Tube Railings

    - Section 05120 – Structural Steel

  - REFERENCES

    - AISC M016 Manual of Steel Construction, Allowed Stress Design

    - ASTM A 36/A 36M Standard Specification for Structural Steel

    - ASTM A123 (Standard Specification for Zinc coating – Hot Dip Galvanizing of Iron and Steel Products)

    - Joint Surface Preparation, SSPC-3, Power Tool Cleaning

    - American Society for Testing and Materials (ASTM) - ASTM A36 Standard Specification for Carbon Structural Steel

    - American Iron and Steel Institute (AISI) - AISI CL 304.

    - American Welding Society Structural Welding Code (AWS) - AWS D1.1, D1.2

  - DESIGN / PERFORMANCE REQUIRMENTS

    - The HatchSafe® provides a permanent, four-sided railing with self closing gate to guard roof hatch/floor openings.

    - HatchSafe® meets applicable OSHA Standards to include 1910.23 and 1910.27.

  - SUBMITTALS

    - Submit under provisions of Section 01300.

    - Product Data:  Manufacturer's data sheets on each product to be used, including:

      - Preparation instructions and recommendations.

      - Storage and handling requirements and recommendations.

      - Installation instructions.

    - Shop Drawings: Provide shop drawings showing layout, profiles, and product components, including anchorage, hardware, and finishes.  Include dimensional plans, applicable material specifications, elevations and sections detailing mounting and connections.

    - Closeout Submittals:  Provide Operation and Maintenance data to include methods for maintaining installed products, precautions against cleaning materials and methods detrimental to finishes and performance.

  - QUALITY ASSURANCE

    - Experience:  Manufacturer must demonstrate a minimum of Five (5) years successful experience in design and manufacture of similar related products.

    - Provide evidence to the effect, including list of installations, descriptions, name and method of contact shall be provided, upon request.

    - Welder Qualifications:  Welders Certified in accordance with American Welding Society Procedures:  AWS-1-GMAW-S, WPS No. B2.004.90 for applicable material used in production of specified product.

  - DELIVER, STORAGE, AND HANDLING

    - Delivery

      - Deliver materials in manufacturer’s original, unopened, undamaged shipping container with identification labels intact.

    - Storage

      - Store all materials in a dry, controlled area to protect from elements and damage.  If outdoor storage is required, block materials to store at an incline, to prevent pooling of any moisture and promote runoff.

      - Do not tarp tightly, as this will entrap moisture.  Instead, tarp materials in a tent-like arrangement, elevated above the product with open sides to allow airflow.

      - For additional questions on delivery, storage, or handling, contact the manufacturer at (877) 446-1519 or (701) 746-4519 or email to 4psinfo@psdoors.com.

    - Handling

      - Use caution when unloading and handling product to avoid bending, denting, crushing, or other damage to the product.

      - When using forklifts, use forks of proper length to fully support product being moved.

  - WARRANTY

    - Special Warranty

      - The manufacturer warranties this product and components to be free from manufacturing defects for a period of one (1) year from ship date.

  - MAINTENANCE

    - Routine inspections and maintenance (Determined by owner).

    - General housekeeping of immediate area.

    - Immediate replacement or repair of damaged or missing components.

- PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer: PS DOORS, 1150 S. 48th Street, Grand Forks, ND  58201.   Phone Toll Free: 877-446-1519. Phone: 701-746-4519. Fax: 701-746-8340.               Web Site: www.psdoors.com. E-mail: 4psinfo@psdoors.com.

    - Substitutions:  Not permitted.

    - Obtain all HatchSafe® assemblies from single manufacturer.

  - EQUIPMENT

    - Products Details:

      - HatchSafe® is a full railing system providing four-sided, permanent protection for guarding roof hatch/floor openings.  Includes self closing safety gate at entry to ensure no openings are left unprotected, and integrated horizontal grab bars.  HatchSafe® consists of a top rail, mid-rail, self-closing swing gate, and horizontal grab bars.  Note:  Roof hatch curb acts as toeboard.  Available in powder coat gray finish.

      - Model/Operation Options:

| Model | Access Width* | Length* |
| --- | --- | --- |
| HSF-4848M | 30”x30” | 48”x48” |
| HSF-4866M | 30”x48” | 48”x66” |
| HSF-4884M | 30”x66” | 48”x84” |
| HSF-5448M | 48”x30” | 54”x48” |
| HSF-5466M | 48”x48” | 54”x66” |
| HSF-5484M | 48”x66” | 54”x84” |

*Outside roof hatch dimensions

      - Material requirements:  See Section 2.3 MATERIALS.

  - MATERIALS

    - Attributes

      - HatchSAFE® to be fabricated from structural or formed steel shapes, tubing -ASTM A513; formatting- ASTM-A-556 Grade B; bar/plate -ASTM-A-36, of appropriate size and strength, welded construction.

      - Finish on all exposed surfaces to be powder coat gray.

  - FABRICATION

    - Fit and shop assemble items in largest practical sections, for delivery to site.

    - Fabricate items with joints tightly fitted and secured.

    - Supply components required for anchorage of fabrications. Fabricate anchors and related components of same material and finish as fabrication, except where specifically noted otherwise.

- EXECUTION

  - EXAMINATION

    - Compliance:  Comply with all manufacturer’s product data, including installations instructions, Operation and Maintenance manuals, reference drawings, shipping and handling, and storage instructions.

  - PREPARATION

    - Clean surfaces thoroughly prior to installation.

    - Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

  - INSTALLATION/APPLICATION

    - HatchSAFE® Installation

      - Install in accordance with manufacturer’s installation instructions, shop drawings, and details.

      - All bolted connections must be tight with no fewer than two threads exposed and the nuts are to be positively locked by provide lock nuts.

    - Tolerances

      - All dimensional requirements must be in accordance with manufacturer’s installation instructions and shop drawings.

  - FIELD QUALITY CONTROL

    - Installation:  Product to be installed using good general construction methods and practices, in accordance with manufacturer’s instructions and drawings.

    - Field Tests/Installation Verification:

      - Verify all anchorage is in accordance with manufacture’s installation instructions and applicable data sheets.

  - CLEANING

    - Repair or replace damaged installed products or components.

    - Touch up damaged finish.

  - PROTECTION

    - Protect installed product and finish surfaces from damage during handling, storage, and installation.

    - Protect installed product and finish surfaces during normal and general use.

END OF SECTION